## Slide 1
O-RAN srsRAN FALCON Extension
Dual-Network Architecture: Data Plane & Metrics Separation
175.0.0.0/8 (oran-intel) - Data Plane (F1AP / F1U / N2 / ZMQ)
171.0.0.0/8 (telemetry-net) - Metrics Collection (UDP → InfluxDB → Grafana)
Setup Commands: docker network create --subnet=175.0.0.0/8 oran-intel docker network create --subnet=171.0.0.0/8 telemetry-net

## Slide 2
Network Topology - Dual Subnet Architecture
175.0.0.0/8 (oran-intel) - DATA PLANE
5GC 175.53.1.2
cu0 175.53.10.1 2nd: .1.11
cu1 175.53.10.2 2nd: .1.12
cu2 175.53.10.3 2nd: .1.15
du0 .1.10
du1 .1.13
du2 .1.14
du3 .1.16
du4 .1.17
du5 .1.18
ue0 .2.1
ue1 .3.1
ue2 .4.1
ue3 .5.1
ue4 .6.1
ue5 .7.1
Redis: 175.24.0.1
Protocols: N2(SCTP:38412), F1AP(SCTP:38472), F1U(UDP), ZMQ(TCP) between DU<->UE
171.0.0.0/8 (telemetry-net) - METRICS PLANE
metrics-server 171.40.1.4:55555
influxdb 171.40.1.5:8086
grafana 171.40.1.6:3000
cu0 171.53.10.1
cu1 171.53.10.2
cu2 171.53.10.3
du0 171.53.1.10
du1 171.53.1.13
du2 171.53.1.14
du3 171.53.1.16
du4 171.53.1.17
du5 171.53.1.18
Flow: DU/CU → UDP:55555 → metrics-server → influxdb → grafana All DU/CU containers are dual-homed: eth0 = oran-intel (priority: 1000) eth1 = telemetry-net (priority: 100) Metrics-only containers (metrics-server, influxdb, grafana) are on telemetry-net ONLY — isolated from data plane.

## Slide 3
Complete IP Address Assignment Table
Container oran-intel (eth0) telemetry-net (eth1) Role ───────── ───────────────── ────────────────── ────────────────── 5GC 175.53.1.2 - 5G Core (AMF/UPF) cu0 175.53.10.1 + .1.11* 171.53.10.1 CU (gnb_id: 511) cu1 175.53.10.2 + .1.12* 171.53.10.2 CU (gnb_id: 512) cu2 175.53.10.3 + .1.15* 171.53.10.3 CU (gnb_id: 513) du0 175.53.1.10 171.53.1.10 DU → cu0 du1 175.53.1.13 171.53.1.13 DU → cu0 du2 175.53.1.14 171.53.1.14 DU → cu1 du3 175.53.1.16 171.53.1.16 DU → cu2 du4 175.53.1.17 171.53.1.17 DU → cu2 du5 175.53.1.18 171.53.1.18 DU → cu2 ue0 175.53.2.1 - UE → du0 ue1 175.53.3.1 - UE → du1 ue2 175.53.4.1 - UE → du2 ue3 175.53.5.1 - UE → du3 ue4 175.53.6.1 - UE → du4 ue5 175.53.7.1 - UE → du5 redis 175.24.0.1 - Cache metrics-server - 171.40.1.4 Metric collector influxdb - 171.40.1.5 Time-series DB grafana - 171.40.1.6 Dashboard * = secondary IP added via entrypoint.sh (dynamic interface detection)

## Slide 4
Container Interface Assignment & tc Packet Loss
DUAL-HOMED CONTAINER (e.g., srsdu0) ┌─────────────────────────────────────────────────────────┐ │ │ │ eth0 (oran-intel) eth1 (telemetry-net) │ │ IP: 175.53.1.10 IP: 171.53.1.10 │ │ priority: 1000 (HIGH) priority: 100 (LOW) │ │ │ │ │ │ ┌───┴────────────┐ ┌──────┴──────────┐ │ │ │ DATA PLANE │ │ METRICS │ │ │ │ │ │ │ │ │ │ • F1AP → CU │ │ • UDP:55555 → │ │ │ │ (SCTP:38472) │ │ metrics-server │ │ │ │ • F1U → CU │ │ (171.40.1.4) │ │ │ │ (UDP) │ │ │ │ │ │ • ZMQ → UE │ │ JSON metrics │ │ │ │ (TCP) │ │ every 500ms │ │ │ └────────────────┘ └──────────────────┘ │ │ │ │ tc qdisc replace dev eth0 ← CORRECT TARGET │ │ root netem loss X% (affects data plane) │ │ │ └─────────────────────────────────────────────────────────┘ WHY priority MATTERS: ───────────────────── Docker assigns interfaces ALPHABETICALLY by network name: "telemetry-net" (m) < "oran-intel" (o) → eth0 would be telemetry-net! Fix: priority: 1000 on oran-intel forces it to be eth0 priority: 100 on telemetry-net makes it eth1 This ensures: • tc on eth0 = affects srsRAN data plane traffic • Metrics flow on eth1 = unaffected by tc experiments

## Slide 5
Why tc Packet Loss Does NOT Trigger HARQ in ZMQ Mode
REAL 5G (over-the-air): ZMQ SIMULATION (this setup): UE DU UE DU ┌────┐ ┌────┐ ┌────┐ ┌────┐ │ APP│ │ │ │ APP│ │ │ │ TCP│ │ │ │ TCP│ │ │ │ IP │ │ │ │ IP │ │ │ │PDCP│ │PDCP│ │PDCP│ │PDCP│ │RLC │ │RLC │ │RLC │ │RLC │ │MAC │◄─►│MAC │ ← HARQ here │MAC │◄──────►│MAC │ ← HARQ here │PHY │◄─►│PHY │ │PHY │ │PHY │ └────┘ └────┘ └──┬─┘ └──┬─┘ ▲ radio ▲ │ ZMQ(TCP) │ └────────┘ └──────┬──────┘ noise → CRC fail │ → HARQ NACK ┌─────┴──────┐ → retransmit │ Linux net │ ← tc operates HERE │ (IP/TCP) │ └────────────┘ PROBLEM: tc drops IP packet ↓ TCP detects loss, retransmits SILENTLY ↓ ZMQ receives complete data ↓ PHY gets PERFECT IQ samples ↓ MAC decodes perfectly → NO HARQ needed RESULT: HARQ = 0 always in ZMQ mode regardless of tc loss Bitrate keeps INCREASING (scheduler sees 0% BLER → raises MCS) TO TRIGGER HARQ: Need PHY-level channel model (AWGN noise), not tc

## Slide 6
What tc CAN Affect: F1U (DU ↔ CU) User Plane
When tc is applied on eth0 (oran-intel) of a DU container: ┌────────┐ tc netem loss X% ┌────────┐ │ DU │──────── eth0 (175.x.x.x) ────────│ CU │ │ │ F1U = UDP (no retx!) │ │ │ │ F1AP = SCTP (has retx) │ │ └────────┘ └────────┘ EFFECT ON F1U (UDP): ──────────────────── • F1U uses UDP → NO automatic retransmission • Dropped F1U packets = lost user plane data • RLC layer detects gaps → RLC retransmissions increase • PDCP may also trigger retransmissions • Overall throughput/bitrate DECREASES EFFECT ON F1AP (SCTP): ────────────────────── • F1AP uses SCTP → HAS retransmission • Control plane messages survive tc loss (with delay) • DU-CU connection stays alive EFFECT ON ZMQ (DU ↔ UE): ───────────────────────── • ZMQ uses TCP → HAS retransmission • Air interface samples survive tc loss • HARQ still won't trigger (PHY sees perfect data) CONCLUSION: ─────────── tc on eth0 will cause: ✓ Bitrate drop (F1U packet loss) ✓ RLC retransmissions increase ✗ HARQ retransmissions (still zero - ZMQ is perfect) Metrics collection on eth1 remains UNAFFECTED.

## Slide 7
Docker Compose File Structure
┌─────────────────────────────────────────────────────────────────────┐ │ docker-compose-cu++.yaml │ │ • 5GC (open5gs) - oran-intel only │ │ • cu0, cu1, cu2 - oran-intel (pri:1000) + telemetry-net (pri:100)│ │ • entrypoint.sh - adds secondary 175.x IP (dynamic iface) │ └─────────────────────────────────────────────────────────────────────┘ ┌─────────────────────────────────────────────────────────────────────┐ │ docker-compose-du.yaml │ │ • du0-du5 - oran-intel (pri:1000) + telemetry-net (pri:100)│ │ • redis - oran-intel only │ └─────────────────────────────────────────────────────────────────────┘ ┌─────────────────────────────────────────────────────────────────────┐ │ docker-compose-ue++.yaml │ │ • ue0-ue5 - oran-intel only │ │ • metrics-server - telemetry-net only (171.40.1.4) │ │ • influxdb - telemetry-net only (171.40.1.5) │ │ • grafana - telemetry-net only (171.40.1.6) │ │ • redis - oran-intel only │ └─────────────────────────────────────────────────────────────────────┘ Config files changed: ───────────────────── • RAN/du_zmq*.conf → metrics addr: 171.40.1.4 (was 175.40.1.4) • RAN/cu_*.yml → metrics addr: 171.40.1.4 (was 175.40.1.4) • RAN/entrypoint_*.sh → dynamic iface detection (was hardcoded eth0)